| Aircraft serial no. RSUK/MT03/ RSUK/MTOS/ | Aircraft 100hr/Annual Repetitive Service Worksheet NB: Take note of hours/time related actions | Aircraft registration no: G- Worksheet date: Worksheet type: 100HR / ANNUAL (delete as appropriate) |
| --- | --- | --- |
|  | Unique worksheet no. (if required/used): |  |
| Task No | Task Description | Repetition or comments | Actions taken & comment | Cert initial |
| Purpose of this worksheet: To be applied after the first 100hrs of operation, and every subsequent 100hrs, or Annually whichever is appropriate. Refer to Maintenance Manuals RSUK0012 and RSUK0044. For aircraft fitted with the in flight variable pitch Woodcomp SR3000/3 prop, additionally refer to Propeller Manual RSUK0076 and Propeller Service Sheet F117. Most of the checks and serviceability are ‘on condition’, meaning the Engineer has the responsibility to decide if it is acceptable for service. The task numbers listed in the left-most column are rationalised i.e. identical on all MT-series Service Worksheets. The task numbers may not be sequential |
|  | Airframe Inspection | All items – repeat inspections as shown unless stated otherwise |  |  |
| 1 | Check - Bolt torques – mast fittings | M8 bolts to 25Nm+5/-1Nm |  |  |
| 2 | Check - Bolt security – other |  |  |  |
| 3 | Inspect - Wheel bearings smooth operation (3 places) | Wheel bearings sealed for life. Raise aircraft with jack under rear keel. |  |  |
| 4 | Op/C - nosewheel fork for straightness and free operation. | MT-03 - Nosewheel fork must rotate freely to the limit stops with respect to the steering link plate. There must be 2-4Nm friction to limit shimmy. MTOsport – nose wheel must pivot freely. |  |  |
| 5 | Inspect nosewheel springs for security and signs of fretting/imminent breakage. | If in doubt, replace springs (MT-03 only). |  |  |
| 6 | Inspect - landing gear spar and attachments to airframe for damage or fatigue (cracks & deformation). | If any cracks or deformation found then ground aircraft and contact RSUK immediately Remove and inspect the four attachment bolts at least every 2 years, one at a time. Replace if corroded. |  |  |
| 7 | Inspect – tyres for wear or damage. Replace if needed. | No fabric to show through the tread area. Recommended 0.5mm min tread No cracks in side-walls |  |  |
| 8 | Check - tyre pressures & tyre creep (mainwheels 1,5 to 2,2bar if heavily loaded, nose 1,5 to 1,8bar) |  | Pressures OK Nose Main LH Main RH |  |
| 9 | Change brake fluid | Recommended at 3years, or when brakes become spongy. Refill from master cylinder with callipers immersed in fluid. If system is spongy after bleeding, check discs for flatness and wheel bolts for straightness. | (on condition) |  |
| 10 | Inspect - airframe for damage, twisting, buckling, or other deformation, or cracks, especially at welded joints at bottom of the mast. | If found ground aircraft and call RSUK for advice. Use of crack detection fluid at base of mast is appropriate to ensure a thorough check is done. |  |  |
| 11 | Inspect - External structure of enclosure sound and firmly fixed to airframe |  |  |  |
| 12 | Inspect – security of landing light shield (if fitted) | Accessible through luggage hatch |  |  |
|  | Electrical/instruments |  |  |  |
| 14 | Inspect - panel connections for security |  |  |  |
| 15 | Inspect – gel battery for leakage | Replace battery after 10 years operation |  |  |
| 16 | Op/C Check strobe function if fitted |  |  |  |
| 17 | Op/C check nav light function if fitted |  |  |  |
| 18 | Op/C check backup fuel pump functions |  |  |  |
| 19 | Op/C check landing light function if fitted |  |  |  |
|  | Rotor head |  |  |  |
| 20 | Time-related 1500hr: Renew main bearing | Replace bearing at 1500hrs (no extension permitted). Bearing bolt torque 150Nm+/-10Nm (plus split pin) NOTE: when tightening hub onto backing plate ensure that the clearance between the main gear and bendix gear is minimised to between 0.05 and 0.15mm Glue bearing temp sensor in with hot melt adhesive. Clearance of rotor speed sensor to gear is 1 to 2mm (confirm function via tacho) |  | 1st inspection Name: Pilot or auth no. Sig 2nd inspection Name: Pilot or auth no. Sig |
| 21 | Check split pin present and no sign of chaffing or looseness. If present, check nut torque and replace split pin. | Second signature required if pin replaced |  | 1st inspection Name: Pilot or auth no. Sig 2nd inspection Name: Pilot or auth no. Sig |
| 22 | Op/C - Ring gear security and bolt attachment | Note any wear patterns Bolt torque is 25Nm |  |  |
| 23 | Check, Service/lube - teeter bolt & bearings for damage & wear. | Regrease via nipple on top of rotor (where fitted). Grease with Castrol LM or equivalent . Removal, clean, inspect and refit is recommended every 100hrs. If wear or signs of distress, remove rotor assembly, inspect and replace bushes or bolt if required. Clean, regrease & refit. NB: Excess wear is more than 0.5mm of vertical play, bolt to bushes, and will cause rotor vibration. Nut must not be more than finger tight, about 1 to 2Nm, and the bolt able to turn by hand. |  | 1st inspection Name: Pilot or auth no. Sig 2nd inspection Name: Pilot or auth no. Sig |
| 24 | Check, bushes in tower sides. If worn, replace | Small sideways float between hub bar and bushes required for low vibration |  |  |
| 25 | Time related 100hr: Service/lube –gimbal joints, check for wear & regrease. | Grease with Castrol LM or equivalent. If wear evident or noticeable looseness, disassemble gimbal joints, check for wear, regrease and reassemble. Torque up bolts to clamp side plates to gimbal block. Back off bolts by 1/4 turn. & fit split pin. Strip and inspect recommended every 200hrs of operation |  | 1st inspection Name: Pilot or auth no. Sig 2nd inspection Name: Pilot or auth no. Sig |
| 26 | Check four split pins present and secure | Main bearing, teeter bolt, pitch and roll bolts. Required even if no disassembly actions. |  |  |
| 27 | Lubricate Bendix gear & spiral gear | WD40 or similar |  |  |
| 28 | Lubricate rotor brake pivot. | WD40 or similar |  |  |
| 29 | Inspect - brake pad for function & wear | Change pad and backplate as one unit (service item) |  |  |
| 30 | Op/C - Check Trim cylinder for free function and slider damage or excess seal leakage. | Seal service kit is available from RSUK |  |  |
| 31 | Protect bare metal with Motor Plus, WD40, chain wax or equivalent |  |  |  |
|  | Rotor Head Controls |  |  |  |
| 35 | Service/lube - clean rod ends (if appropriate) |  |  |  |
| 36 | F/C - control rod ends for cracks & freedom of movement both free and at control extremes |  |  |  |
| 37 | F/C- rotor head reaches pitch and roll stops |  |  |  |
| 38 | Inspect - all tubes straight, all bearings free, all bearing retaining rivets secure |  | 48 rivets |  |
| 39 | Op/C - for free play in stick control eg bearings or wear |  |  |  |
|  | Rudder controls |  |  |  |
| 40 | Op/C - Check pedals for ease of movement |  |  |  |
| 41 | Inspect for cable freedom of movement at tail and pedal attachment, and turnbuckle wirelocking |  |  |  |
| 42 | Inspect - rudder cables for frays, corrosion, wear or chaffing (particularly between the fuel cross over tube and the cables), and nico sleeves for signs of movement. |  |  |  |
| 43 | Inspect - tail bearings for looseness and freedom of operation |  |  |  |
| 44 | Inspect - tail for security to airframe (4 bolts, 15Nm) | Loctited – if loose, remove and refit with loctite 243. Check to 12Nm |  |  |
| 45 | Inspect tail and rudder for signs of composite damage. | Include waggling the side fin in case of internal structural damage. |  |  |
| 46 | Inspect - all cable pulleys for free rotation, security & wear | Check |  |  |
| 47 | Inspect – rudder to tail fastenings | Check to 12Nm | Confirm if possible rudder offset to pedals |  |
| 48 | Inspect – security of rudder trim tab |  |  |  |
| 49 | F/C rudder control cable tension | For limits and methods see manual | Gauge no. Reading |  |
|  | Inspect – that all rod end joints are fitted with a snubbing failsafe washer. |  |  |
| 51 | Check that all control system bolts are correct items, properly fitted and tight |  |  |
|  | Intentionally blank | Intentionally blank | Intentionally blank |
| 55 | Engine NOTE! All engine checks to be in accordance with manufacturers manual! | For engine servicing refer to the engine manual issued with the aircraft (Rotax 912ULS or 914UL). The full annual engine service is required only when no engine servicing has been carried out in the last 12 months. Otherwise apply ‘on condition’. Servicing must be carried out in line with, and recorded on, the Rotax service schedule contained within the ‘Line Maintenance’ manual for the engine fitted. |  |
| 56 | Wirelocking – ensure present on oil tank drain plug, aftermuffler, Oil banjo under engine, carb air filters, oil pump |  |  |
| 57 | Engine service fasteners | If the magnetic inspection plug or the crankshaft locking screw plug are disturbed then any wire-locking present must be properly reinstated |  |
|  | Service/lube - Lubricate carburettor choke levers if no free movement | HSC2000 spray grease or equivalent |  |  |
| 59 | Service/lube - Ensure choke and throttles move freely from stop to stop, and that turbo detent can be felt correctly. Ensure cables are synchronised. |  |  |  |
| 60 | Inspect – engine mount rubbers for deterioration |  |  |  |
| 61 | Inspect engine bearer bolts for paint stripe, and if moved, re loctite and tighten to 35Nm. Otherwise check bolt torque. Re-apply paint stripe as required. | See SB-10 |  |  |
|  | Intentionally blank | Intentionally blank | Intentionally blank | Intentionally blank |
|  | Fuel system |  |  |  |
| 65 | Service/lube – Drain any water in the fuel tanks via the water drain valves, confirming correct function and closure. Drain crossover tube via drain plug only if water found in main tanks. | Seal thread with PTFE tape or equivalent, ensuring minimal overlap over the plug end. Wirelock after refitting |  | 1st inspection Name: Pilot or auth no. Sig 2nd inspection Name: Pilot or auth no. Sig |
| 66 | Op/C functionality of low-fuel warning light (if fitted) | Using a siphon tube or fuel-grade pump drain tanks to near empty (less than 5 litres). Change fuel level over sensor by tipping a/c on to its tail. Low fuel warning when sensor not covered, no warning when sensor is covered. Replenish fuel after test. |  |  |
| 67 | Service/lube - Change or clean fuel filter (gauze filter before mechanical and electrical fuel pumps, KL145 paper filter only after electrical pumps) if dirty | Filter change only required if obviously dirty. Always change pre and post pump filters as a set. Recommended at 500hrs/3yrs. |  |  |
| 68 | Inspect - fuel tank caps for seal deterioration & security of fit |  |  |  |
| 69 | Inspect – security of fuel tanks and tightness of tank straps | Fuel tanks must not be deformed by straps. Adjust to suit – it should be just possible for the tank to move under hand loading |  |  |
| 70 | Op/C - functionality of fuel gauge | ie that the reading matches that shown on the tank sight gauge. | Early types are push-before reading, later types electrically driven continuous display |  |
| 71 | Inspect - breather pipe filter for blockage. |  |  |  |
| 72 | Replace breather pipe filter | Recommended at 3yrs, or on condition |  |  |
| 73 | Inspect - inside tanks for debris cracks and deterioration | Flush as required |  |  |
| 74 | Inspect - all hoses for cracks and deterioration |  |  |  |
|  | Pre rotator |  |  |  |
| 80 | Inspect- drive shafts for bend or damage and belt for splits or damage | Lubricate belt with silicon spray, PTFE spray or talcum powder if stick slip found. Replace belt when insufficient tension under pressure to operate pre rotator. |  |  |
| 81 | Op/C – Cycle by hand thru full range – check drive shaft joints for free movement and bearings for play etc, and that return spring is undamaged |  |  |  |
| 82 | Inspect – security of pneumatic cylinder and mountings/safety restraint wire |  |  |  |
| 83 | Inspect - pre rotator gearbox mounting bracket, esp around bolts to gearbox for cracks or fractures |  |  |  |
| 84 | Inspect - universal joints for corrosion | Clean as required (use a kitchen plastic scouring pad) and spray with oil or chain wax |  |  |
| 85 | Inspect - drive unit engagement to rotor drive gear. | Do not grease this unit! – very light oil only or it will start to jam. |  |  |
| 86 | Op/C - Wheel brake for function – if wheel rotates freely, turn brake rubber thru 90 degrees to correct function. Replace when worn with service part. |  |  |  |
| 87 | Inspect - Ensure slider shafts move freely, and are greased | Check horizontal shaft by pushing pulley wheel with hand and checking for slider free movement. |  |  |
| 88 | Inspect - Pull back slider gaiter and ensure shaft is well lubricated and no corrosion. Check gaiter for splits and replace if needed. | If gaiter is split, it must be replaced. Jamming of the vertical slider would have catastrophic consequences in flight! |  |  |
|  | Trim System, Rotor Brake & Pneumatics |  |  |  |
| 90 | Inspect – all hoses for leaks and slave cylinder for looseness |  |  |  |
| 91 | Op/C – Roll trim. Operate roll trim (where fitted) fully left. Force to hold stick central ~0.5 to 1Kg. Ensure panel indicator shows fully left. Then operate trim fully right. Ensure indicator shows fully right | Trim load may be adjusted by shortening or lengthening bungy cord under right side of pilots seat – do not adjust without consulting pilot, as the loads required are small! |  |  |
| 92 | Time-related 100hr: Change (or dry out) compressor water absorber |  |  |  |
| 93 | Inspect – compressor. Listen for undue noises in operation. |  |  |  |
| 94 | Op/C - Full functional check pneumatic system – refer as required to the maintenance manual for fault finding and rectification, and a more comprehensive understanding of the test background. | With selector set to ‘Brake’ position, engage brake by pressing button, confirm operation, and that function is acceptable. Pressurise to maximum. Change to flight – check for 2 to 3 sec max to release air from brake system). In ‘Flight’ position check that trim goes on and off in same direction as button (inc rear switch if fitted). In ‘Flight’ position, stick forward. Start pre rotator. Ensure cylinders (2) engage, and when the stick is pulled back they disengage. Note that the head cylinder must engage prior to the engine cylinder. Stick to front, release pre rotator and confirm that pressure is applied to trim and stick comes back slightly. In ‘Brake’ position, put 3 bar pressure on and ensure pre rotator does not function Press the ‘Interlock release button’ and ensure that pre rotator functions (both cylinders, head and engine) with brake engaged. |  |  |
| 95 | Op/C – check compressor can give full pressure of 7bar (~8bar with new compressor). If under 5.5bar, either find leak or replace. |  | Note pressure obtained |  |
|  | HTC Propeller (for Woodcomp refer to RSUK0076) |  |  |  |
| 96 | F/C - tracking to manufacturers recommendations | (none required at the time of writing) |  |  |
| 97 | Check - prop bolt torques, and that torque stripe between bolt head and propeller hub has not been broken (indicating that the bolt has slackened). If missing, apply stripe to each of the six bolts holding the prop to the engine. | 15Nm, loctite centre 6 bolts. If loose, remove, inspect, and refit with loctite 243 | Does NOT apply to Woodcomp propeller! |  |
| 98 | Measure prop blade pitch angle relative to hub | Recommend pitch to be within 0.5deg of each other | Blade 1 Blade 2 Blade 3 Hub |  |
| 99 | Inspect - blades to manufacturers recommendations for any damage, splits etc. Repair only as manufactures recommendations | Take care with water ingress into propeller blades. If necessary rotate slowly to drain water |  |  |
| 100 | Inspect – prop tape (if fitted) for air-bubbles, lifted edges or deterioration | Replace as needed - refer to Maintenance Manual |  |  |
|  | Rotors |  |  |  |
| 105A | Rotor system with black end-cap (8.4m) or grey end-cap (8.0m) rotor-blades Remove rotor from aircraft and place on suitable trestles on the rotor side, such that the blade is under negligible bending load. Remove rotor blades from hub bar if required. Check blades for straightness axially in the area of the outboard bolt hole with a 1m straight edge | These blades are life limited to 700hrs. No bend permissible This check is carried out every 100hrs and is not required annually |  |  |
| 105 B | RotorSystemII with red end-cap rotor-blades Remove rotor from aircraft. Remove rotor blades from hub bar Clean carefully and degrease the inspection area, noting any evidence of fretting (a black dust or residue). Then check blade underside around outboard bolt hole area (to +/-60mm axially along the blade) for cracks with a x5 magnifier. Check blades for straightness axially in the area of the outboard bolt hole with a 1m straight edge. | These blades are life limited to 2,500hrs. This check is carried out every 500hrs to 1500hrs, then every 100hrs to 2,500hrs. No cracks permissible. No bend permissible. Carefully inspect the blade and hub bar bolt hole areas, refer to SIL-028. If any evidence of fretting is noted, contact RSUK for advice/action required. Replace bolts/nuts as required |  |  |
| 106 | Inspect - blades to manufacturers recommendations for any damage, splits etc. | Repair only as manufacturer’s recommendations |  |  |
| 107 | Check and inspect the blade to hub bar, and hub bar assembly bolts for corrosion | Every 2yrs or 100hrs. Remove and replace the bolts sequentially. Full disassembly may adversely affect the rotor balance. Lubricate bolts with HHS2000 or equiv. Replace bolts/nuts as required |  |  |
| 108 | Refitment of rotors Check - torques on blade to hub bar bolts/nuts (20+/-5Nm). Check Teeter bolt finger tight at 1-2Nm, free to rotate by hand. Grease via the grease nipple | If any evidence of blade to hub looseness, disassemble blades from hub bar. Check holes for wear or fretting Refer to Section 9 General Notes of the Maintenance Manual for nyloc re-usage. Use new split pin in teeter-bolt. |  |  |
| 109 | If no teeter bolt grease nipple fitted: Service/lube –disassemble rotor from rotor head , check for wear, regrease by hand and reassemble. | Grease nipple (approved mod) may be fitted. Grease Castrol LM or equivalent |  |  |
|  | Other |  |  |  |
| 110 | Inspect - for wheel-brake pad wear. Replace as necessary, and if less than 2mm pad remaining (later pads have witness groove). | If calipers are sticking or uneven wear is found, loosen/turn wheel bolts and check for straightness – if OK retighten. Alternatively, clean brake pad bushes & lubricate calipers around seal |  |  |
| 111 | Inspect – brake ratchet/pawl for excessive wear. If found, replace lever and pawl. | Teeth of lever must not be visibly deformed or protrude less than 1.5mm. |  |  |
| 112 | Inspect - Confirm all placards readable and in line with Operating Limitations | See Pilots handbooks for placards required – or TADs |  |  |
| 113 | Check aircraft weight and balance | No annual check required, but confirm weighing certificate available and matches weight on placard |  |  |
| 114 | Inspect all seat belt attachment points for tightness and security |  |  |  |
| 115 | Inspect each seat belt for damage or frays, and for security of main connection |  |  |  |
| 116 | F/C - ASI calibration | That front and rear ASI readings match. ASI reading checked on flight test or alternative method |  |  |
| 117 | F/C – compass calibration | Typically cross check to handheld compass |  |  |
| 118 | F/C – altimeter calibration | Consistent with ambient pressure |  |  |
| 119 | Op/C – Avionics checks | Transponder - Check that mode S code matches G-INFO database. At each bi-annual inspection a full functional check is required, using an Aeroflex IFR6000 test-set or equivalent to confirm correct transponder function including correlation with a/c altimeter. Radio – confirm PTT buttons cause ‘T’ on panel. (NB: Further checked for transmit and receive quality on Annual flight-test) Turbo TCU data (where fitted) may be downloaded for analysis | Transponder code required to be transmitted: Actual code transmitted transponder code: Where possible, print out transponder test report and attach to service docs |  |
|  | Final ground run checks prior to release |  |  |  |
| 130 | Inspect - Power plant and coolant system for leaks |  |  |  |
| 131 | Inspect – security of oil-thermostat insulator pad (if fitted) |  |  |  |
| 132 | Inspect – instruments for measurements consistent with ambient conditions |  |  |  |
| 133 | Inspect – all access covers secure |  |  |  |
| 134 | Securely tie aircraft down and run to full power. Ensure engine rpm achieves at least 5,400 on one fuel pump only, and with both pumps running. |  | RPM achieved: |  |
| 135 | Complete mag drop checks at 4,000rpm | See Pilots Handbook for limits | Mag drop: |  |
| 136 | Confirm ‘Gen’ light is on when engine not running, and off (or flickering gently) when running at above 2000rpm. |  |  |  |
| 137 | Confirm low fuel lamp is not lit (providing the fuel covers the sensor) |  |  |  |
| 138 | If a VP propeller is fitted, cycle the propeller manually from pitch stops to pitch stop. Ensure warning led lights when operating, and function is as per Pilots Handbook. | Prop must stop on electrical limit switches, not the mechanical failsafe stops. |  |  |
| 139 | Ensure all log book entries completed appropriately, and service record up to date |  |  |  |
| Confirm Service bulletins incorporated (from RSUK website, full list available with applicability) The list at the time of this document issue is stated to the right. | SB-001 (914Turbo only) RPM gauge green line to finish at 5,000rpm (914UL’s) SB-002 Cable ferrule crimping (one time inspection. Completed) SB-003 Breather tube routing (serial 16 to 49) SB-004 Bendix shaft (serial 27 to 49) SB-006 Battery link (applies to all MT-03’s) SB-007 Rudder cable alignment (applies to all MT-03’s) SB-008 Fuel pickup re route (applies to all MT-03’s) SB-009 Front seat reinforcement (applies to all MT-03’s) SB-010 Engine bearer bolt SB-012 Fuel hose SB-013 Suspension bow change (500Kg upgrade) SB-014 MTOsport enclosure bracket repair SB-016 MT-03 enclosure bracket repair SB-017 Control panel blanking plugs SB-018 Front pedal position alteration SB-019 Instructor pack fitment SB-021 Woodcomp VP Prop and CS controller (MTOS) SB-022 912ULS exhaust springs SB-023 Landing-light shield SB-024 LED landing lights SB-027 Pre-rotator improvement kit SB-028 Low level fuel sensor SB-033 Rotax plug screw wire-locking SB-034 Rotor blade check (MANDATORY ALL AIRCRAFT) SB-036 Oil thermostat insulator SB-037 Relocated fuel transfer pipe (MT03) SB-038 Propeller protection tape SB-040 MT-series new rotor system |  |
| Confirm Mandatory Permit Directives incorporated (from CAA website, CAP747 and 661) The list at the time of this document issue is stated to right. Up-to-date information must be checked! | MPD 1998-019 R1 Clear hose on the 914UL return fuel line (check for flexibility, ongoing requirement) MPD 2010-001Inspection/replacement of Trelleborg Hydro K Hoses MPD 2010-005 R1 Replacement of Honeywell low fuel warning sensor (mandatory for MTOS/024-036 inc only) MPD 2011-006 Life limit of rotor blade assembly |  |
| CAP 747 Document date or issue checked, plus notes: |  |  |
| CAP 661 Document date or issue checked, plus notes: |  |  |
| EASA MPD or AD check (EASA website): note date checked and any actions required |  |  |
| Confirm compliance to BG01 Type Approval Data Sheet (TADS) for the MT-03, or BG02 Type Approval Data Sheet (TADS) for the MTOsport. Note any non-compliances and actions taken. |  |  |
| Tasks completed by (name): Signature: Initial: (to compare to Date: check sheet) | Engine hours logged: Airframe hours logged: Aircraft hourmeter hrs logged: |
| The technical content of this document is approved under the authority of the UK CAA Design Organisation Approval Ref: DAI/9917/06 |
| Permit Maintenance Release: The work recorded above (all pages) has been completed to my satisfaction and in that respect the aircraft is considered fit for flight. Signature: Initial: (to compare to Date: check sheet) Inspector or licence no.: Company Approval ref Inspector Authority: CAA/LAA/other ref dated | Comments: |
| Note to Engineer; remember to reference this worksheet and RSUK0012 or RSUK0044 within the logbooks, together with your Authority authorisation code. Work undertaken may be noted on this worksheet, or if required on another sheet (such as F093) also referenced in the logbook. Modifications undertaken must be noted with their MC approval no. Check the back pages to complete these too for modifications, service bulletins, MPDs, etc. |